## Slide 1: Speedtrack System
Monitoring & controlling vehicle speed

## Slide 2: INTRODUCTION
The aim of the speedtrack using 8051
1. Measure and display speed
2. Provide a reliable speed monitoring system
3. Enhance safety and efficiency

## Slide 3: System components
✧ AT89C51
✧ IR Obstacle sensor
✧ LM016L
✧ Logictoggle
✧ Led-Red

## Slide 4: IR Obstacle Sensor
IR sensors help the Speedtrack System detect obstacles and measure distance. They use infrared light to find how close objects are, ensuring safe movement.
This Photo by Unknown Author is licensed under CC BY-NC-ND

## Slide 5: Microcontroller AT89C51
The AT89C51 is an 8-bit microcontroller with 4KB Flash and 128B RAM. It's reliable and versatile, ideal for control tasks in the Speedtrack System.

## Slide 6: LCD Display (LM016L)
The LM016L LCD is a character display used in the Speedtrack System for clear alphanumeric output. Its backlight and reliability improve user interaction and visibility.

## Slide 7
BLOCK DIAGRAM
IR 2
IR 1
AT89C51
LED-RED
LCD
TOGGLE
TOGGLE

## Slide 8
CIRCUIT DIAGRAM

## Slide 9
1. INITIALIZATION :
* Turn of the LED
* Initialize the LED
2. Loop continuously :
* Monitor IR sensors to detect when a car enters the zone
CODE LOGIC
Car cross IR1 :
if(IR1 == 1) {
while(IR2 == 0) {
delay(100);
Time++;
}
}

## Slide 10: Speed check : if(speed >72) { led = 1; lcd_string(“OVER SPEED”); led = 0; } else { lcd_string(“NORMAL SPEED”) } SAME LOGIC IF IR2 TRIGGERED : else if (IR2 == 1) { while(IR1 == 0) { Delay(100); Time++; } }

## Slide 11: OUTPUTS

## Slide 15: Advantages of Speed Track System
Accurate Speed Measurement: Provides precise speed data.
2. Real-time Monitoring: Enables immediate feedback and action
3. Reliability: 8051 microcontroller ensures stable performance.
4. Cost-Effective: Relatively low-cost solution

## Slide 16
conclusion
In conclusion, the Speedtrack System uses key parts like the AT89C51 microcontroller, LM016L LCD, IR sensors, and logic toggles. Each part helps the system work smoothly and adjust to different needs. Knowing how
these parts work helps get the best use out of the system.

## Slide 17
THANK YOU!